## Slide 1: CSCI 4430 - Fall 23
Tutorial 11

## Slide 2: Intra-Domain Routing
Routing Protocols
  Link-State (LS) Routing
    Open Shortest Path First (OSPF)
    Dijkstra’s Algorithm
  Distance-Vector (DV) Routing
    Routing Information Protocol (RIP)
    Bellman-Ford Algorithm
  * Routing Protocols are used by routers to exchange network information about topology and routing, but not the encapsulated protocols and payload inside data packets.

## Slide 3: Q1 True/False
Link-State (LS) routing involves broadcasting its local knowledge of the network to everyone.
True; uses Dijkstra’s for computation (OSPF).
Conversely, Distance-Vector routing involves telling only neighbors about its global view.
True; uses Bellman-Ford for computation (RIP).
Both routing methods involve finding least-cost paths to all other nodes.
True; both are the shortest path calculation algorithm that allows easy metric to avoid loops.

## Slide 4: Q2 Link-State Routing: Dijkstra
1 Initialization:
2 N' = {u}; D(u) = 0
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N':
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 least path cost to w plus cost from w to v */
15 until all nodes are in N'
If adjacent, set to its cost;
If not, set to infinity
Insert current min cost node, update costs,
Until all nodes inserted

## Slide 5: Q2 Link-State Routing: Dijkstra
Update: D(v) = min( D(v), D(w) + c(w,v) )
Init: if v adjacent to u then D(v) = c(u,v) else D(v) = ∞
Step | N’ | D(b), p(b) | D(c), p(c) | D(d), p(d) | D(e), p(e)
0 | a |  |  |  | 
1 |  |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
Calculate shortest paths start from a to all nodes

## Slide 6: Q2 Link-State Routing: Dijkstra
Init: if v adjacent to u then D(v) = c(u,v) else D(v) = ∞
Step | N’ | D(b), p(b) | D(c), p(c) | D(d), p(d) | D(e), p(e)
0 | a | 10,a | ∞,a | 30,a | 100,a
1 | a,b |  |  |  | 
2 |  |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
Calculate shortest paths start from a to all nodes

## Slide 7: Q2 Link-State Routing: Dijkstra
Step | N’ | D(b), p(b) | D(c), p(c) | D(d), p(d) | D(e), p(e)
0 | a | 10,a | ∞,a | 30,a | 100,a
1 | a,b |  | 60,b | 30,a | 100,a
2 | a,b,d |  |  |  | 
3 |  |  |  |  | 
4 |  |  |  |  | 
Update: D(v) = min( D(v), D(w) + c(w,v) )
W = b
Calculate shortest paths start from a to all nodes

## Slide 8: Q2 Link-State Routing: Dijkstra
Step | N’ | D(b), p(b) | D(c), p(c) | D(d), p(d) | D(e), p(e)
0 | a | 10,a | ∞,a | 30,a | 100,a
1 | a,b |  | 60,b | 30,a | 100,a
2 | a,b,d |  | 50,d |  | 90,d
3 | a,b,d,c |  |  |  | 
4 |  |  |  |  | 
Update: D(v) = min( D(v), D(w) + c(w,v) )
W = d
Calculate shortest paths start from a to all nodes

## Slide 9: Q2 Link-State Routing: Dijkstra
Step | N’ | D(b), p(b) | D(c), p(c) | D(d), p(d) | D(e), p(e)
0 | a | 10,a | ∞,a | 30,a | 100,a
1 | a,b |  | 60,b | 30,a | 100,a
2 | a,b,d |  | 50,d |  | 90,d
3 | a,b,d,c |  |  |  | 60,c
4 | a,b,d,c,e |  |  |  | 
Update: D(v) = min( D(v), D(w) + c(w,v) )
W = c
Calculate shortest paths start from a to all nodes

## Slide 10: Q2 Link-State Routing: Dijkstra
Step | N’ | D(b), p(b) | D(c), p(c) | D(d), p(d) | D(e), p(e)
0 | a | 10,a | ∞,a | 30,a | 100,a
1 | a,b |  | 60,b | 30,a | 100,a
2 | a,b,d |  | 50,d |  | 90,d
3 | a,b,d,c |  |  |  | 60,c
4 | a,b,d,c,e |  |  |  | 
Update: D(v) = min( D(v), D(w) + c(w,v) )
a-b, cost: 10
a-d-c, cost: 50
a-d, cost: 30
a-d-c-e, cost: 60
W = e
Calculate shortest paths start from a to all nodes

## Slide 11: Q3 Distance-Vector Routing: Bellman-Ford
Bellman-Ford Equation
  let dx(y) := cost of least-cost path from x to y c(x, v) := cost to neighbor v
  then dx(y) = minv {c(x, v) + dv(y)} over all neighbors v of x

## Slide 12: Q3 Distance-Vector Routing: Bellman-Ford
dx(y) = minv {c(x, v) + dv(y)}

## Slide 13: Q3 Distance-Vector Routing: Bellman-Ford
dx(y) = minv {c(x, v) + dv(y)}

## Slide 14: Q3 Distance-Vector Routing: Bellman-Ford
dx(y) = minv {c(x, v) + dv(y)}

## Slide 15
Thanks!