## Slide 1: CSCI4430 Computer Networks Lecture 13: Network Layer – Inter-domain Routing
Hong Xu, Henry
CSE@CUHK, 2025
Material with thanks to Patrick Lee, Mosharaf Chowdhury, Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Context and terminology
“End hosts”
“Clients”, “Users”
“End points”
“Interior Routers”
“Autonomous System (AS)” or “Domain” Region of a network under a single administrative entity
“Route” or “Path”
“Border Routers”

## Slide 3: AS-level Internet
Internet Inter-Domain Traffic, SIGCOMM, 2010

## Slide 4: Autonomous systems (AS)
An AS is a network under a single administrative control
  Currently over 70,000 ASes
  Updated daily at https://www.cidr-report.org/as2.0/
ASes are sometimes called “domains”
Each AS is assigned a unique identifier (ASN)
  E.g., CUHK owns ASN 3661

## Slide 5: “Intra-domain” routing: Within an AS
Link-State (e.g., OSPF) and Distance-Vector (e.g., RIP)
Primary focus
  Finding least-cost paths
  Fast convergence

## Slide 6: “Inter-domain” routing: Between ASes
Two key challenges
  Scaling
  Administrative structure
    Issues of autonomy, policy, privacy

## Slide 7: Recall: Addressing (so far)
Each host has a unique ID
No particular structure to those IDs

## Slide 8: Recall: Forwarding
111010010
MIT
#1
#2
#3
#4
Dst | Next Hop
UMICH | 1
UCB | 3
MIT | 2
NYU | 4
#0
Forwarding Table @ #0
To UMich
To MIT
To UCB
To NYU

## Slide 9: Two key challenges
Scaling
Administrative structure
  Issues of autonomy, policy, privacy

## Slide 10: Scaling
A router must be able to reach any destination
  Given packet’s dst address, look up the next hop
Naive: Have an entry for each destination
  There would be over 108 entries!
  AND routing updates per destination!
How can we improve scalability?
  An example: longest-prefix matching (see backup slides)

## Slide 11: A smaller table at node B?
Destination | Next Hop
to 1 | A
to 2 | C
to 3 | C
to 4 | A
to 5 | C
to 6 | A
to 7 | A
to 8 | C
1
7
4
6
A
B
C
2
5
8
3

## Slide 12: Re-number the end-systems?
Careful address assignment  can aggregate multiple addresses into one range  scalability!
Akin to reducing the number of destinations
Destination | Next Hop
to [1-4] | A
to [5-8] | C
1
3
4
2
A
B
C
6
5
8
7

## Slide 13: Scaling
A router must be able to reach any destination
Naive: Have an entry for each destination
Better: Have an entry for a range of addresses
  Can’t do this if addresses are assigned randomly!
  How addresses are allocated will matter!
Host addressing is key to scaling

## Slide 14: Two key challenges
Scaling
Administrative structure
  Issues of autonomy, policy, privacy

## Slide 15: Administrative structure shapes inter-domain routing
ASes want freedom in picking routes
  “My traffic can’t be carried over my competitor’s network”
  “I don’t want to carry A’s traffic through my network”
  Not expressible as Internet-wide “least cost”
ASes want autonomy
  Want to choose their own internal routing protocol
  Want to choose their own policy
ASes want privacy
  Choice of network topology, routing policies, etc.

## Slide 16: Choice of routing algorithm
Link-state
  No privacy – broadcasts all network information
  Limited autonomy – needs agreement on metric, algo
Distance-vector is a decent starting point
  Per-destination updates give some control
  BUT wasn’t designed to implement policy
  AND is vulnerable to loops
The “Border Gateway Protocol” (BGP) extends distance-vector ideas to accommodate policy

## Slide 17: Agenda
Inter-domain-routing
  Addressing (Scalability)
  BGP (Autonomy, policy, privacy)
    Context and basic ideas
    Details and issues

## Slide 18: IP addressing

## Slide 19: Goal of addressing: Scalable routing
State: Small forwarding tables at routers
  Much less than the number of hosts
Churn: Limited rate of change in routing tables
Ability to aggregate addresses is crucial for both

## Slide 20: Aggregation works if…
Groups of destinations reached via the same path
These groups are assigned contiguous addresses
These groups are relatively stable
Few enough groups to make forwarding easy
1
3
4
2
A
B
C
6
5
8
7

## Slide 21: IP addressing is hierarchical
Hierarchical address structure
Hierarchical address allocation
Hierarchical addresses and routing scalability

## Slide 22: IP addresses (IPv4)
Unique 32-bit number associated with a host
Represented with the “dotted-decimal” notation
  e.g., 12.34.158.5
00001100
00100010
10011110
00000101
12
34
158
5
00001100
00100010
10011110
00000101

## Slide 23: Hierarchy in IP addressing
32 bits are partitioned into prefix and suffix
Prefix is the network component; suffix is the host component
Inter-domain routing operates on network prefix
00001100
00100010
10011110
00000101
Network (23 bits)
Host (9 bits)
12
34
158
5

## Slide 24: CIDR: Classless inter-domain routing
Flexible division between network and host addresses
Offers a better tradeoff between size of the routing table and efficient use of the IP address space

## Slide 25: CIDR example
Suppose a network has 50 computers
  Allocate 6 bits for host addresses (25 < 50 < 26)
  Remaining 32 - 6 = 26 bits as network prefix
Flexible boundary means the boundary must be explicitly specified with the network address!
  Informally, “slash 26”  128.23.9.8/26
  Formally, prefix represented with a 32-bit mask: 255.255.255.192, where all network prefix bits set to “1” and host suffix bits to “0”
  Also known as subnet mask (a group of machines with the same prefix are in the same subnet)

## Slide 26: Before CIDR: Classful addressing
Three classes
  8-bit network prefix (Class A),
  16-bit network prefix (Class B), or
  24-bit network prefix (Class C)
Example: an organization needs 500 addresses.
  A single class C address is not enough (<500 hosts)
  Instead, a class B address is allocated (~65K hosts)
    Huge waste!

## Slide 27: IP addressing is hierarchical
Hierarchical address structure
Hierarchical address allocation
Hierarchical addresses and routing scalability

## Slide 28: Allocation done hierarchically
Internet Corporation for Assigned Names and Numbers (ICANN) gives large blocks to…
Regional Internet Registries, such as the American Registry for Internet Names (ARIN), which give blocks to…
Large institutions (ISPs), which give addresses to…
Individuals and smaller institutions
FAKE Example:
  ICANN  ARIN  AT&T  UMICH  EECS

## Slide 29: CIDR: Addresses allocated in contiguous prefix chunks
Recursively break down chunks as get closer to host
12.0.0.0/8
12.0.0.0/15
12.253.0.0/16
12.2.0.0/16
12.3.0.0/16
:
:
12.3.0.0/22
12.3.4.0/24
:
:
12.3.254.0/23
12.253.0.0/19
12.253.32.0/19
12.253.64.0/19
12.253.64.108/30
12.253.96.0/18
12.253.128.0/17
:
:
:
:

## Slide 30: FAKE example in more detail
ICANN gave ARIN several /8s
ARIN gave AT&T one /8, 12.0/8
  Network Prefix: 00001100
AT&T gave UMICH a /16, 12.34/16
  Network Prefix: 0000110000100010
UMICH gave EECS a /24, 12.34.56/24
  Network Prefix: 000011000010001000111000
EECS gave me specific address 12.34.56.78
  Address: 00001100001000100011100001001110

## Slide 31: IP addressing is hierarchical
Hierarchical address structure
Hierarchical address allocation
Hierarchical addresses and routing scalability

## Slide 32: IP addressing  Scalable routing?
Hierarchical address allocation only helps routing scalability if allocation matches topological hierarchy

## Slide 33: IP addressing  Scalable routing?
AT&T a.0.0.0/8
France Telecom
UMICH-D a.b.0.0/16
UMICH-AA a.c.0.0/16
a.c.*.* is this way
a.b.*.* is this way

## Slide 34: IP addressing  Scalable routing?
AT&T a.0.0.0/8
France Telecom
UMICH-D a.b.0.0/16
UMICH-AA a.c.0.0/16
a.*.*.* is this way
foo.com a.d.0.0/16
Can add new hosts/networks without updating
the routing entries at France Telecom

## Slide 35: IP addressing  Scalable routing?
AT&T a.0.0.0/8
UMICH-D a.b.0.0/16
UMICH-AA a.c.0.0/16
ESNet
ESNet must maintain routing entries for both a.*.*.* and a.c.*.*

## Slide 36: IP addressing  Scalable routing?
Hierarchical address allocation only helps routing scalability if allocation matches topological hierarchy
May not be able to aggregate addresses for “multi-homed” networks
  A multi-homed network is connected to more than one ASes for fault-tolerance, load balancing, etc.

## Slide 37: BGP: Border Gateway Protocol

## Slide 38: BGP
The role of policy
  What we mean by it
  Why we need it
Overall approach
  Four non-trivial changes to DV
Policies
Mechanism

## Slide 39: Administrative structure shapes Inter-domain routing
ASes want freedom to pick routes based on policy
ASes want autonomy
ASes want privacy

## Slide 40: Topology & policy shaped by inter-AS business relationship
Three basic kinds of relationships between ASes
  AS A can be AS B’s customer
  AS A can be AS B’s provider
  AS A can be AS B’s peer
Business implications
  Customer pays provider
  Peers don’t pay each other
    Exchange roughly equal traffic
Notes: Ehy???

## Slide 41: Business relationships
peer
peer
provider
customer
Relations between ASes
Customers pay provider
Peers don’t pay each other
Business implications

## Slide 42: Why peer?
A
B
C
D
E
D and E communicate a lot
Peering saves B and C money

## Slide 43: Routing follows the money!
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer
traffic allowed
traffic not allowed
ASes provide “transit” between their customers
Peers do not provide transit between other peers

## Slide 44: Routing follows the money!
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer
An AS only carries traffic to/from its own customers over a peering link

## Slide 45: Routing follows the money!
A
B
E
Pr
Cu
Peer
Peer
Routes are “valley” free (more details later)

## Slide 46: In short
AS topology reflects business relationships between ASes
Business relationships between ASes impact which routes are acceptable

## Slide 47: BGP
The role of policy
  What we mean by it
  Why we need it
Overall approach
  Four non-trivial changes to DV

## Slide 48: Inter-domain routing: Setup
Destinations are IP prefixes (12.0.0.0/8)
Nodes are Autonomous Systems (ASes)
  Internals of each AS are hidden
Links represent both physical links and business relationships
BGP (Border Gateway Protocol) is the Inter-domain routing protocol
  Implemented by AS border routers

## Slide 49: BGP: Basic idea
Each AS selects the “best” route it hears advertised for a prefix
An AS advertises (“exports”) its best routes to each IP prefix
You’ve heard this story before!
Notes: Arrows are routing message

## Slide 50: BGP inspired by Distance-Vector
Per-destination route advertisements
No global sharing of network topology information
Iterative and distributed convergence on paths
With four crucial differences!

## Slide 51: BGP & DV differences: (1) Not picking shortest-path routes
BGP selects the best route based on policy, not shortest distance (i.e., least-cost)
AS A may prefer “A,B,C” over “A,C”
How do we avoid loops?
A
B
C

## Slide 52: BGP & DV differences: (2) Path-Vector routing
Key idea: advertise the entire path
  Distance vector: send distance metric per dest d
  Path vector: send the entire path for each dest d
C
B
A
d
“d: path (B,A)”
“d: path (A)”
data traffic
data traffic

## Slide 53: BGP & DV differences: (2) Path-Vector routing
Key idea: advertise the entire path
  Distance vector: send distance metric per destination
  Path vector: send the entire path for each destination
Benefits
  Loop avoidance is straightforward (simply discard paths with loops)
  Flexible and expressive policies based on entire path

## Slide 54: BGP & DV differences: (3) Selective route advertisement
For policy reasons, an AS may choose not to advertise a route to a destination
Hence, reachability is not guaranteed even if graph is physically connected
A
B
C
AS-C does not want to carry traffic to AS-B

## Slide 55: BGP & DV differences: (4) BGP may aggregate routes
For scalability, BGP may aggregate routes for different prefixes
AT&T a.0.0.0/8
France Telecom
UMICH-D a.b.0.0/16
UMICH-AA a.c.0.0/16
a.*.*.* is this way
foo.com a.d.0.0/16

## Slide 56: BGP policies

## Slide 57: Policy dictates how routes are “selected” and “exported”
Selection: Which path to use?
  Controls whether/how traffic leaves the network
Export: Which path to advertise?
  Controls whether/how traffic enters the network
Can reach 128.3/16
blah blah
Route selection
A
P
C
B
Q
Route export
Notes: Arrows: routing messages!

## Slide 58: Typical selection policies
In decreasing order of priority
  Make/save money (send to customer > peer > provider)
  Maximize performance (shortest AS path length)
  Minimize use of my network bandwidth (“hot potato”)
  …

## Slide 59: Typical export policy
Destination prefix advertised by… | Export route to…
Customer | Everyone (providers, peers, other customers)
Peer | Customers
Provider | Customers
We’ll refer to these as the “Gao-Rexford” rules
(capture common – but not required! – practice)

## Slide 60: Gao-Rexford
Peers
Providers
Customers
With Gao-Rexford, the AS policy graph is a DAG (directed acyclic graph) and routes are “valley free”

## Slide 61: BGP Protocol details

## Slide 62: Who speaks BGP?
Border router
Border routers in an Autonomous System
Internal router

## Slide 63: What does “speak BGP” mean?
Implement the BGP protocol standard
  Read more here: http://tools.ietf.org/html/rfc4271
Specifies what messages to exchange with other BGP “speakers”
  Message types (e.g., route advertisements, updates)
  Message syntax
How to process these messages
  E.g., “when you receive a BGP update, do…. “
  Follows BGP state machine in the protocol spec + policy decisions, etc.

## Slide 64: BGP sessions: External
Border routers in an AS speaks BGP with border routers in other ASes using eBGP sessions

## Slide 65: BGP sessions: Internal
A border routers speaks BGP with other routers in the same AS using iBGP sessions

## Slide 66: eBGP, iBGP, and IGP
eBGP: BGP sessions between border routers in different ASes
  Learn routes to external destinations
iBGP: BGP sessions between border routers and other routers within the same AS
  Distribute externally learned routes internally
IGP: “Interior Gateway Protocol” = Intra-domain routing protocol
  Provide internal reachability
  E.g., OSPF, RIP

## Slide 67: eBGP, iBGP, and IGP together
Learn routes to external destinations using eBGP
Distribute externally learned routes internally using iBGP
Travel shortest path to egress using IGP

## Slide 68: Basic messages in BGP
Open
  Establishes BGP session (BGP uses TCP)
Notification
  Report unusual conditions
Update
  Inform neighbor of new routes
  Inform neighbor of old routes that become inactive
Keep-alive
  Inform neighbor that connection is still viable

## Slide 69: Route updates
Format <IP prefix: route attributes>
  Attributes describe properties of the route
Two kinds of updates
  Announcements: new routes or changes to existing routes
  Withdrawal: remove routes that no longer exist

## Slide 70: Route attributes
Routes are described using attributes
  Used in route selection/export decisions
Some attributes are local
  I.e., private within an AS, not included in announcements
Some attributes are propagated with eBGP route announcements
There are many standardized attributes in BGP
  We will discuss just two

## Slide 71: Attributes: (1) ASPATH
Carried in route announcements
Vector that lists all the ASes a route advertisement has traversed (in reverse order)
AS 7018
AT&T
AS 12654
128.112.0.0/16
AS path = 7018 88
AS 88
Princeton, 128.112/16
IP prefix = 128.112.0.0/16
AS path = 88

## Slide 72: Attributes: (2) LOCAL PREF
Local preference in choosing between different AS paths
  Local to an AS; carried only in iBGP messages
The higher the value the more preferred
AS4
AS2
AS3
AS1
140.20.1.0/24
BGP table at AS4:
Notes: Because communicated to all IBGP routers within AS, all routers have a common view of how to exit the AS.
This differs from MED in 2 ways: (1) the destination prefix can be anywhere in the internet, not just in the next AS (as in the case for MED). (2) the AS that sets Local_Pref, is also the one that uses it. This allows one node to tell everyone locally what the best way out is.
MED can’t be used in this example because there is exactly one connection between any pair of AS’s.

## Slide 73: Using attributes
Example rules for route selection in priority order
Priority | Rule | Remarks
1 | LOCAL PREF | Pick highest LOCAL PREF
2 | ASPATH | Pick shortest ASPATH length
3 | MED | Lowest MED preferred
4 | eBGP > iBGP | Did AS learn route via eBGP (preferred) or iBGP?
5 | iBGP path | Lowest IGP cost to next hop (egress router)
6 | Router ID | Smallest next-hop router’s IP address as tie-breaker

## Slide 74: BGP UPDATE processing
Best Route
Selection
Apply Import
Policies
Best Route
Table
Apply Export
Policies
forwarding
Entries
BGP
Updates
BGP
Updates
IP Forwarding Table
Open-ended programming.
Constrained only by vendor configuration language
Data plane
Control plane
Data packets
Data packets

## Slide 75: BGP issues in practice

## Slide 76: Issues with BGP
Reachability
Security
Convergence
Performance
Anomalies

## Slide 77: Reachability
In normal routing, if graph is connected then reachability is assured
With policy routing, this does not always hold
AS 2
AS 3
AS 1
Provider
Provider
Customer

## Slide 78: Security
An AS can claim to serve a prefix that they do not have a route to (blackholing)
  Problem not specific to policy or path vector
  Important because of AS autonomy
  Fixable: make ASes “prove” they have a path
AS may forward packets along a route different from what is advertised
  Tell customers about fictitious short path…
  Much harder to fix!
  More: http://queue.acm.org/detail.cfm?id=2668966

## Slide 79: Convergence
If all AS policies follow “Gao-Rexford” rules, BGP is guaranteed to converge
For arbitrary policies, BGP may fail to converge!

## Slide 80: Performance nonissues
Internal routing
  Domains typically use “hot potato” routing
  Not always optimal, but economically expedient
Policy is not always about performance
  Policy-driven paths aren’t the shortest
AS path length can be misleading
  20% of paths inflated by at least 5 router hops
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 81: AS path length can be misleading
An AS may have many router-level hops
AS 4
AS 3
AS 2
AS 1
BGP says that path 4 1 is better than path 3 2 1

## Slide 82: Real performance issue: Slow convergence
BGP outages are the biggest source of Internet problems
Most popular paths are very stable
Outages are still very common
  Check out https://bgpstream.com/
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 83: BGP misconfigurations
BGP protocol is bloated yet underspecified
  Lots of attributes
  Lots of leeway in how to set and interpret attributes
  Necessary to allow autonomy, diverse policies
    But also gives operators plenty of rope
Configuration is mostly manual and ad hoc
  Disjoint per-router configuration to effect AS-wide policy
Notes: Lesson: not being optimal: who cares
Not being connected: we all care!!

## Slide 84: Summary
Two key challenges in inter-domain routing
  Scaling (Addressing)
  Administrative structure (BGP)
    Issues of autonomy, policy, privacy
BGP policies, protocol, and challenges

## Slide 85: Backup slides on longest prefix matching

## Slide 86: Looking up the output port
One entry for each address  4 billion entries!
For scalability, addresses are aggregated
Notes: How does a router determine which output port for the packet!

## Slide 87: Example
Router with 4 ports
Destination address range mapping
  11 00 00 00 to 11 00 00 11: Port 1
  11 00 01 00 to 11 00 01 11: Port 2
  11 00 10 00 to 11 00 11 11: Port 3
  11 01 00 00 to 11 01 11 11: Port 4

## Slide 88: Example
Router with 4 ports
Destination address range mapping
  11 00 00 00 to 11 00 00 11: Port 1
  11 00 01 00 to 11 00 01 11: Port 2
  11 00 10 00 to 11 00 11 11: Port 3
  11 01 00 00 to 11 01 11 11: Port 4

## Slide 89: Longest prefix matching
110000**
110001**
1100****
1101****
ISP Router
Port 1
Port 2
Port 3
Port 4

## Slide 90: Finding match efficiently
Testing each entry to find a match scales poorly
  On average: O(number of entries)
Leverage tree structure of binary strings
  Set up tree-like data structure

## Slide 91: Longest prefix matching
110000**
110001**
1100****
1101****
ISP Router
Port 1
Port 2
Port 3
Port 4

## Slide 92: Tree structure
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
000  Port 1
001  Port 2
0**  Port 3
1**  Port 4
Notes: Idea: build tree to help with match. When a new packet comes in, walk the tree to determine the correct port.
Each level in the tree: one bit. Root: all wild cards

## Slide 93: Tree structure
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
000  Port 1
001  Port 2
0**  Port 3
1**  Port 4
Record port associated with latest match, and only override when it matches another prefix during walk down tree
Notes: Idea: build tree to help with match. When a new packet comes in, walk the tree to determine the correct port.
Each level in the tree: one bit. Root: all wild cards