## Slide 1: CSCI4430 Computer Networks Lecture 15: Link Layer – Ethernet
Hong Xu, Henry
CSE@CUHK, 2023
Material with thanks to Patrick Lee, Mosharaf Chowdhury, Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Data link layer
Present everywhere
Transfers data between adjacent nodes or between nodes on the same local area network
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch

## Slide 3: Link layer
Provides four primary services
  Framing
    Encapsulates network layer data
  Link access
    Medium access control (MAC) protocol defines when to transmit frames
  Reliable delivery
    Primarily for mediums with high error rates (e.g., wireless)
  Error detection or correction

## Slide 4: Packets are now “frames”
Frames encapsulate network layer packets
Link layer protocols are implemented in h/w
Frame formats can change based on link layer protocol
sending
node
frame
receiving
node
data
frame
network
adaptor
network
adaptor
link layer protocol

## Slide 5: Point-to-point vs. broadcast medium
Point-to-point: dedicated pairwise communication
  E.g., long-distance fiber link
  E.g., Point-to-point link b/n Ethernet switch and host
Broadcast: shared wire or medium
  Traditional Ethernet (pre ~2000)
  802.11 wireless LAN

## Slide 6: Multiple access algorithm
Context: a shared broadcast channel
  Must avoid having multiple nodes speaking at once
    Otherwise, collisions lead to garbled data
  Need distributed algorithm to determine which node can transmit
Three classes of techniques
  Channel partitioning: divide channel into pieces
  Taking turns: scheme for deciding who transmits
  Random access: allow collisions, and then recover
    More in the Internet style!

## Slide 7: Random access MAC protocols
When node has packets to send
  Transmit at full channel data rate w/o coordination
Two or more transmitting nodes  collision
  Data lost
Random access MAC protocol specifies
  How to detect and recover from collisions
Examples
  ALOHA and Slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA (wireless)

## Slide 8: Ethernet
Invented as a broadcast technology
  Hosts share channel
  Each packet received by all attached hosts
  CSMA/CD for media access control
Modern Ethernets are “switched” (later)
  Point-to-point links between switches and between a host and switch
  No sharing  no CSMA/CD
    Uses “self learning” and “spanning tree” algorithms for routing

## Slide 9: CSMA
CSMA: Carrier sensing multiple access
CSMA: listen before transmit
  If channel is sensed idle: transmit entire frame
  If channel is sensed busy: defer transmission
Human analogy: don’t interrupt others!
Does not eliminate collisions
  Why?

## Slide 10: CSMA collisions
Propagation delay: two nodes may not hear each other before sending
CSMA reduces but does not eliminate collisions
Collision: entire packet transmission time wasted
  Distance and propagation delay affect collision probability
Spatial layout of nodes

## Slide 11: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  Collisions detected within short time
  Colliding transmissions aborted, reducing wastage
Collision detection easy in wired (broadcast) LANs
  Compare transmitted, received signals
Collision detection difficult in wireless LANs
Notes: wireless: because reception while tx is difficult . broadcast isn’t perfect so collisions local

## Slide 12: Three key ideas of random access
Carrier sense
  Listen before speaking and don’t interrupt
  Checking if someone else is already sending data
  … and waiting till the other node is done
Collision detection
  If someone else starts talking at the same time, stop
    Make sure everyone knows there was a collision!
  Realizing when two nodes are transmitting at once
  …by detecting that the data on the wire is garbled

## Slide 13: Three key ideas of random access
Randomness
  Don’t start talking again right away
  Waiting for a random time before trying again

## Slide 14: How long should you wait?
Should it be immediate?
Should it be a random number with a fixed distribution?

## Slide 15: Ethernet: CSMA/CD Protocol
Carrier sense: wait for link to be idle
Collision detection: listen while transmitting
  No collision: transmission is complete
  Collision: abort transmission & send jam signal
Random access: binary exponential back-off
  After collision, wait a random time before retrying
  After mth collision, choose K randomly from {0, …, 2m-1}
    Wait for K*512 bit times before trying again
    If transmission occurring when ready to send, wait until end of transmission (CSMA)

## Slide 16: Switched Ethernet

## Slide 17: Why switched Ethernet?
Enables concurrent communication
  Host A can talk to C, while B talks to D
  No collisions and no need for CSMA/CD
  No constraints on link lengths, etc.
Ethernet switch
A
B
C
D

## Slide 18: The evolution of Ethernet
Changed almost everything except the frame format
  From 3 Mbit/s to 100 Gbit/s
  From electrical signaling to optical
Lesson: a good interface can accommodate many changes
  Evolve the implementation while maintaining the interface (backward compatibility)

## Slide 19: Turing Award 2022
ACM named Robert Metcalfe receipt of the 2022 Turing Award for “leading the invention, standardization, and commercialization of Ethernet local-area networking technology”
https://awards.acm.org/award-recipients/metcalfe_3968158

## Slide 20: Topics
Frames and framing
Addressing
Routing
Forwarding
Discovery

## Slide 21: Ethernet “Frames”
Encapsulates IP datagram
Preamble: 7 bytes for clock synchronization and 1 byte to indicate start of frame
Addresses: 6 bytes
Type: 2 bytes, higher-layer protocol (e.g., IP)
Data payload: max 1500 bytes, min 46 bytes
CRC: 4 bytes for error detection
type
Preamble
Dst Address
Source Address
Data
CRC

## Slide 22: Topics
Frames and framing
Addressing
Routing
Forwarding
Discovery

## Slide 23: Medium Access Control (MAC) Address
MAC address
  Numerical address associated with a network adapter
  Flat name space of 48 bits (e.g., 00-15-C5-49-04-A9 in HEX)
  Unique, hard-coded in the adapter when it is built
Hierarchical Allocation
  Blocks: assigned to vendors (e.g., Intel) by the IEEE
    First 24 bits (e.g., 00-15-C5-**-**-**)
  Adapter: assigned by the vendor from its block
    Last 24 bits

## Slide 24: MAC address vs. IP address
MAC Addresses
Hard-coded when adapter is built
Flat name space of 48 bits (e.g., 00-0E-9B-6E-49-76)
Like a HK ID
Portable, and can stay the same as the host moves
Used to get packet between interfaces on same network
IP Addresses
Configured, or learned dynamically
Hierarchical name space of 32 bits (e.g., 12.178.66.9)
Like a postal mailing address
Not portable, and depends on where the host is attached
Used to get a packet to destination IP subnet

## Slide 25: Topics
Frames and framing
Addressing
Routing
Forwarding
Discovery

## Slide 26: “Routing” with broadcast Ethernet
Sender transmits frame onto broadcast link
Each receiver’s link layer passes the frame to the network layer:
  If destination address matches the receiver’s MAC address OR if the destination address is the broadcast MAC address (ff:ff:ff:ff:ff:ff)
AMAC
BMAC
CMAC
DMAC
EMAC
FMAC

## Slide 27: “Routing” with broadcast Ethernet
Ethernet is “plug-n-play”
A new host plugs into the Ethernet and is good to go
  No configuration by users or network operators
  Broadcast as a means of bootstrapping communication
AMAC
BMAC
CMAC
DMAC
EMAC
FMAC

## Slide 28: Why does Ethernet not use LS/DV?
Concerns over scalability
  Flat MAC addresses cannot be aggregated like IP addresses
Legacy
  Backward compatibility with broadcast Ethernet
  Desire to maintain Ethernet’s plug-n-play behavior
  How broadcast Ethernet evolved

## Slide 29: Routing in extended LANs
Local-Area Network (LAN)
Bridges relay broadcasts from one LAN to the other

## Slide 30: Easiest way to avoid loops
Use a topology where loops are impossible!
Take an arbitrary topology and build a spanning tree
  Sub-graph that includes all vertices but contains no cycles
  Links not in the spanning tree are not used to forward frames

## Slide 31: Consider a graph

## Slide 32: A spanning tree

## Slide 33: Another spanning tree

## Slide 34: Spanning tree protocol (Perlman’85)
Protocol by which bridges construct a spanning tree
Nice properties
  Zero configuration (by operators or users)
  Self healing
Still used today

## Slide 35: Routing with switched Ethernet?
AMAC
BMAC
CMAC
DMAC
EMAC
FMAC

## Slide 36: Flooding on spanning tree

## Slide 37: Ethernet topics
Frames and framing
Addressing
Routing
Forwarding
Discovery

## Slide 38: But isn’t flooding wasteful?
Yes, but we can use it to bootstrap more efficient forwarding
Idea: watch the packets going by, and learn from them
  If node A sees a packet from node B come in on a particular port, it knows what port to use to reach B!
  Works because there is only one path to B

## Slide 39: Nodes can “learn” routes
Switch learns how to reach nodes by remembering where flooding packets came from
  If flood packet from Node A entered switch on port 4, then switch uses port 4 to send to Node A

## Slide 40: General approach
Flood first packet to node you are trying to reach
All switches learn where you are
When destination responds, some switches learn where it is…
  Only some switches, because packet to you follows direct path, and is not flooded

## Slide 41: Learning from flood packets
Node A
Node A can be reached
through this port
Node A can be reached
through this port
Once a node has sent a flood message, all other switches know how to reach it….
Node B

## Slide 42: Node B responds
Node A
Node B can be reached
through this port
When a node responds, some of the switches learn where it is
Node B
Node B can be reached
through this port
Node B can be reached
through this port
Node B can be reached
through this port

## Slide 43: Ethernet switches are “self learning”
When a packet arrives:
  Inspect source MAC address, associate with incoming port
  Store mapping in the switch table
  Use time-to-live field to eventually forget mapping
A
B
C
D
Packet tells switch how to reach A.

## Slide 44: Link layer topics
Frames and framing
Addressing
Routing
Forwarding
Discovery and bootstrapping

## Slide 45: Discovery
A host is “born” knowing only its MAC address
Must discover lots of information before it can communicate with a remote host B
  What is my IP address?
  What is B’s IP address? (remote)
  What is B’s MAC address? (if B is local)
  What is my first-hop router’s address? (if B is not local)
  …

## Slide 46: ARP and DHCP
Link layer discovery protocols
  ARP  Address Resolution Protocol
  DHCP  Dynamic Host Configuration Protocol
  Confined to a single local-area network (LAN)
  Rely on broadcast capability
Hosts
Router

## Slide 47: ARP and DHCP
Link layer discovery protocols
Serve two functions
  Discovery of local end-hosts
  Bootstrap communication with remote hosts
    What’s my IP address?
    Who/where is my local DNS server?
    Who/where is my first hop router?

## Slide 48: DHCP
Dynamic Host Configuration Protocol
  Defined in RFC 2131
A host uses DHCP to discover
  Its own IP address
  Its netmask
  IP address(es) for its local DNS name server(s)
  IP address(es) for its first-hop “default” router(s)

## Slide 49: Are we there yet?
DHCP Server
DNS Server
Router
Host
Host
Host
Host
What I learnt from DHCP
my IP: 1.2.3.48
netmask: 1.2.3.0/24 (255.255.255.0)
Local DNS: 1.2.3.156
router: 1.2.3.19

## Slide 50: Sending packets over link Layer
Link layer only understands MAC addresses
  Translate the destination IP address to MAC address
  Encapsulate the IP packet in a link-level (Ethernet) frame
Router
Host
Host
Host
Host
DNS
1.2.3.48
1.2.3.156
58-23-D7-FA-20-B0
90-E2-A1-09-66-1B
1.2.3.53
1.2.3.156
IP packet

## Slide 51: ARP: Address Resolution Protocol
Every host maintains an ARP table
  List of (IP address  MAC address) pairs
Consult the table when sending a packet
  Map dest. IP address to dest. MAC address
  Encapsulate (IP) data packet with MAC header; xmit
What if IP address not in the table?
  Sender broadcasts: Who has IP address 1.2.3.156?
  Receiver replies: MAC address 58-23-D7-FA-20-B0
  Sender caches result in its ARP table

## Slide 52: What if the destination is remote?
Look up the MAC address of the first hop router
  1.2.3.48 uses ARP to find MAC address for first-hop router 1.2.3.19 rather than ultimate destination IP address
How does the red host know the destination is not local?
  Uses netmask (discovered via DHCP)
How does the red host know about 1.2.3.19?
  Also DHCP
host
host
DNS
...
host
host
host
...
router
router
1.2.3.0/24 (255.255.255.0)
5.6.7.0/24
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 53: Key ideas in both ARP and DHCP
Broadcasting: Can use broadcast to make contact
  Scalable because of limited size
Caching: remember the past for a while
  Store the information you learn to reduce overhead
Soft state: eventually forget the past
  Associate a time-to-live field with the information
  … and either refresh or discard the information
  Key for robustness in the face of unpredictable change

## Slide 54: ID resolution in networking
Layer | Examples | Structure | Configuration | Resolution Service
App. Layer | cse.umich.edu | Organizational hierarchy | ~ manual | 
Network Layer | 123.45.6.78 | topological hierarchy | DHCP | 
Link layer | 45-CC-4E-12-F0-97 | vendor (flat) | hard-coded | 
DNS
ARP

## Slide 55: Discovery mechanisms
We have seen two approaches
  Broadcast (ARP, DHCP)
    Flooding does not scale
    No centralized point of failure
    Zero configuration
  Directory service (DNS)
    No flooding = scalable
    Root of the directory is vulnerable (caching is key)
    Needs configuration to bootstrap (local, root servers, etc.)

## Slide 56: Summary
Data link layer transfers data between adjacent nodes or nodes connected to the same switch
Ethernet evolved from a broadcast medium to switched
Spanning tree enables Ethernet to efficiently flood a network to learn routes while forwarding packets
DHCP and ARP form the discovery backplane of networking and make everything work together

## Slide 57: Additional slides

## Slide 58: CSMA/CD (Collision Detection)
For this to work, need restrictions on minimum frame size and maximum distance
  Why?
Spatial layout of nodes

## Slide 59: Limits on CSMA/CD network length
Latency depends on physical length of link
  Time to propagate a frame from one end to other
Suppose A sends a frame at time t
  And B sees an idle line at a time just before t + d
  … so B happily starts transmitting a frame
B detects a collision, and sends jamming signal
  But A cannot see collision until t + 2d
latency d
A
B

## Slide 60: Limits on CSMA/CD network length
A needs to wait for time 2d to detect collision
  So, A should keep transmitting during this period
  AND keep an eye out for a possible collision
Imposes restrictions; e.g., for 10 Mbps Ethernet
  Maximum length of the wire: 2,500 meters
  Minimum length of a frame: 512 bits (64 bytes)
latency d
A
B

## Slide 61: Framing frames
Physical layer puts bits on a link
But, two hosts connected on the same physical medium need to be able to exchange frames
  Service provided by the link layer
  Implemented by the network adaptor
Framing problem: how does the link layer determine where each frame begins and ends?

## Slide 62: Simple approach: Count bytes
Sender includes number of bytes in header
  Receiver extracts this number of bytes of body
What if the Count field is corrupted?
  L2 will frame the wrong bytes  a framing error
  CRC tells you to discard this frame, but what about the next one?
53
Body
80
Body
53 bytes of data
80 bytes of data
61
Body
80
Body
61 bytes of data misdelivered
??? bytes of data misdelivered
???
Bogus count field

## Slide 63: Desynchronization
Once framing on a link is desynchronized, it can stay that way
Need a method to resynchronize

## Slide 64: Framing with sentinel bits
Delineate frame with special “sentinel” bit pattern
  e.g., 01111110  start, 01111111  end
What if sentinel occurs within frame?
Solution: bit stuffing
  Sender always inserts a 0 after five 1s in the frame contents
  Receiver always removes a 0 appearing after five 1s
01111110
01111111
Frame contents
Notes: 6 one’s  start
7 one’s  end

## Slide 65: When receiver sees five 1s…
If next bit 0, remove it; begin counting again
  Because this must be a stuffed bit; we can’t be at beginning/end of frame (those had six or seven 1s)
If next bit 1 (i.e., we’ve seen six 1s) then:
  If following bit is 0, this is start of frame
    Because the receiver has seen 01111110
  If following bit is 1, this is end of frame
    Because the receiver has seen 01111111
01111110
01111111
Frame content

## Slide 66: Example: sentinel bits
Original data, including start/end of frame:
  01111110011111101111101111100101111111
Sender rule: five 1s  insert a 0
  After bit stuffing at the sender:
  01111110011111010111110011111000101111111
Receiver rule: five 1s and next bit 0  remove 0
  01111110011111101111101111100101111111

## Slide 67: Self learning: Handling misses
When packet arrives with unfamiliar destination
Forward packet out all other ports
Response may teach switch about that destination
A
B
C
D

## Slide 68: Contrast
IP
Packets forwarded on all available links
Addresses can be aggregated
Routing protocol computes loop-free paths
Forwarding table computed by routing protocol
Ethernet
Packets forwarded on subset of links (spanning tree)
Flat addresses
“Routing” protocol computes loop-free topology
Forwarding table derived from data packets(+ spanning tree for floods)

## Slide 69: DHCP: Operation
One or more local DHCP servers maintain required information
  IP address pool, netmask, DNS servers, etc.
  Application that listens on UDP port 67

## Slide 70: DHCP: Operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
  L2 broadcast, to MAC address FF:FF:FF:FF:FF:FF

## Slide 71: DHCP: Operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message
  Proposed IP address for client, lease time
  Other parameters

## Slide 72: DHCP: Operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message
Client broadcasts a DHCP request message
  Specifies which offer it wants
  Echoes accepted parameters
  Other DHCP servers learn they were not chosen

## Slide 73: DHCP: Operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message
Client broadcasts a DHCP request message
Selected DHCP server responds with an ACK

## Slide 74: DHCP: Operation
One or more local DHCP servers maintain required information
Client broadcasts a DHCP discovery message
One or more DHCP servers responds with a DHCP “offer” message
Client broadcasts a DHCP request message
Selected DHCP server responds with an ACK
DHCP “relay agents” used when the DHCP server is not on the same broadcast domain

## Slide 75: DHCP uses “soft state”
Soft state: if not refreshed, state is forgotten
  Hard state: allocation/revocation is deliberate
Implementation:
  Address allocations have a lease period
  Server sets a timer for each allocation
  Client must request a refresh before lease expires
  Server resets timer when a refresh arrives and ACKs
    OR reclaims allocated address when timer expires
Simple, yet robust under failure