## Slide 1: CSCI 4430 – Spring 25
Tutorial 12

## Slide 2: Routing
Intra-Domain Routing
  OSPF
    Link State
  RIP
    Distance Vector
IGP = Interior Gateway Protocol
Inter-Domain Routing
  BGP = Border Gateway Protocol
    eBGP = external BGP
    iBGP = internal BGP

## Slide 3: BGP Attributes
Priority | Rule | Remarks
1 | LOCAL PREF | Pick highest LOCAL PREF (AS egress router)
2 | ASPATH | Pick shortest ASPATH length
3 | MED | Lowest MED preferred (AS ingress router)
4 | eBGP > iBGP | Prefer via eBGP announcements over iBGP
5 | iBGP path | Lowest IGP cost to next hop (internal egress router)
6 | Router ID | Prefer lowest BGP neighbor router ID, serve as tie break

## Slide 4: Q1
In the given network, suppose AS2 and AS3 are running OSPF for their intra-AS routing protocol. Suppose AS1 and AS4 are running RIP for their intra-AS routing protocol. Suppose eBGP and iBGP are used for the inter-AS routing protocol, and there is no physical link between AS2 and AS4. Assume every link in an AS has the same cost.
● Router 3c learns about prefix x from which routing protocol? eBGP
● Router 3a learns about prefix x from which routing protocol? iBGP
● Router 1c learns about prefix x from which routing protocol? eBGP

## Slide 5: Q1
Once router 1d learns about x it will put an entry (x, I) in its forwarding table.
● Will I be equal to l1 or I2 for this entry? l1
● Now suppose that there is a physical link between AS2 and AS4, shown by the dotted line. Suppose router 1d learns that x is accessible via AS2 as well as via AS3. Will I be set to I1 or I2 ? l2
● Now suppose there is another AS, called AS5, which lies on the path between AS2 and AS4. Suppose router 1d learns that x is accessible via AS2, AS5, AS4 as well as AS3, AS4. Will I be set to I1 or I2 ? l1
ASPATH > iBGP Path

## Slide 6: Q2
Suppose AS X and AS Z are not directly connected but instead are connected by AS Y. Further suppose that X has a peering agreement with Y, and that Y has a peering agreement with Z. Finally, suppose that Z wants to transit all of Y’s traffic but does not want to transit X’s traffic. Does BGP (alone) allow Z to implement this policy?
Yes, AS Z can selectively advertise the routes. AS Z can only advertise the routes it learns from AS Y, but not the routs of AS X that AS Y has learned from AS X.

## Slide 7: Q3
In the given network, ISP B provides national backbone service to regional ISP A. ISP C provides national backbone service to regional ISP D. Each ISP consists of one AS. B and C peer with each other in two places using BGP. Consider traffic going from A to D. B would prefer to handle that traffic over to C on the West Coast (so that C would have to absorb the cost of carrying the traffic cross-country), while C would prefer to get the traffic via its East Coast peering point with B (so B would have carried the traffic across the country). What BGP mechanism might C use so that B would hand over A-to-D traffic at its East Coast peering point?

## Slide 8: MED
● Multi-exit discriminator (MED) is used when ASes are interconnected via 2 or more links; it is used to advertise to neighbors how they should enter our AS.
● MED is exchanged between ASes.
● The lowest MED is the preferred path.
● MED is propagated to all routers within the neighbor AS but not passed along to any other ASes.

## Slide 9: Q3
ISP C wants Router 4 to be the ingress router instead of router 3, so we must have MED4 < MED3, e.g. MED4 = 10, MED3=20

## Slide 10
Thanks!