## Slide 1: CSCI4430 Computer Networks Lecture 1: Intro and Overview
Hong Xu, Henry
CSE@CUHK, 2025
Material with thanks to Mosharaf Chowdhury, Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, Keith Winstein, and many others.

## Slide 2: Agenda
Introduction
Class policies, logistics, and roadmap
Overview of the basics
  How is the network shared?
  How do we evaluate a network?

## Slide 3: Course websites
https://github.com/henryhxu/CSCI4430
https://piazza.com/cuhk.edu.hk/fall2025/csci4430estr4120
Course materials:
Discussions, Q&A, announcements:
https://blackboard.cuhk.edu.hk/ultra/courses/_221611_1/cl/outline
Marks:

## Slide 4: About me: Hong Xu, Henry
Ph.D. from Toronto
B.Eng. from IE@CUHK, 2003–2007, NA College
Research areas: Computer networks, ML systems
  https://henryhxu.github.io/
Research opportunities available
Office hours: Mon 9–10am, Tue 1–2pm
  By appointment (via Piazza private messages)

## Slide 5: TA team
Yicheng (head TA), Yangtao, Shaofeng
Office hours: check course website
  No office hours this week
Yangtao
Yicheng
Shaofeng

## Slide 6: Prerequisites
CENG3150/CSCI3150, or equivalent OS courses
  If you haven’t taken it or have failed it, you are advised NOT to take this course
  Talk to me if you are not sure
Comfortable with C/C++ programming
Comfortable with Linux

## Slide 7: What is this course about?
The question: How can computers communicate?
  Well, slightly simpler than communication among people…
  Two machines => link
  Multiple machines => network
  Multiple networks => Inter-network => Internet!
What it’s NOT about
  How to design web pages
  How to write web services
  …

## Slide 8: What is a network?
A system of “links” that interconnect “nodes” in order to move “information” across
We will focus primarily on the Internet

## Slide 10: The Internet in 1969

## Slide 11: What did they use it for?
Sending files between scientists: “Here’s a big file of astronomy data!”
Email: “Where shall we have lunch today?”
Remote login to another computer

## Slide 12: 1971

## Slide 13: TCP/IP, HTTP, Web browser
Mosaic, 1993,
Marc Andreessen
TCP, 1974, Vint Cerf & Robert Kahn
HTTP, 1989,
Tim Berners-Lee

## Slide 14: How does it evolve – Now

## Slide 15
How does it all work?
Why was it designed this way?

## Slide 16: Isn’t it really difficult…?
CSCI 4430

## Slide 17: Our goals
To learn how the Internet works.
To learn why the Internet was designed this way.
To learn how to use the Internet.
To build some significant pieces of the Internet.
To learn the underlying principles and technologies of networking.

## Slide 18: What you will learn
The whole stack of layers; details of each layer
Computer network (or the Internet) evolution follows a bottom-up pattern naturally
But you will learn it in a top-down manner
It’s important to keep this difference in mind; many confusions can be understood by remembering this discrepancy
Answer this question: what happens when you enter google.com in your browser

## Slide 19: A little preview…
Quite different from other CS fields
  No unifying framework or theory
  “just a bag of protocols”
    HTTP, IMAP, RTSP, DNS, TCP, UDP, IP, BGP, OSPF, ARP, DHCP, CSMA/CD, …
There is no right or wrong!
Learn the design philosophy and tradeoffs, more than anything else
  There is good and bad design!

## Slide 20: Design matters
Good design
Bad design

## Slide 21: Class workload
Three programming assignments
  First one is an individual assignment
  The rest are in groups of 2
  May have bonus parts
Quizzes
  Randomly pick 5 tutorials to have quiz
  MC or simple calculation, takes <3min
Midterm
Final exam

## Slide 22: Assessment
 | Allocation
Assignment 1 | 10%
Assignment 2 | 15%
Assignment 3 | 20%
Quizzes | 5%
Midterm | 10%
Final Exam | 40%
Bonus in assignments | X%

## Slide 23: Assignments (tentative)
Assignment 1: measure end-to-end throughput and delay of networks (i.e., simple speed test)
Assignment 2: video streaming from CDNs (i.e., simple Netflix)
Assignment 3: reliable transport (i.e., how to transfer data over an unreliable network)

## Slide 24: Communication protocol
Piazza for all communication
  Sign up code “4430_rocks!”
  Do NOT email me or the TA! We may not respond
    Use private messages for private matters
    Only email us when you’re emailed to
Assignment submission via an autograder
  Start forming groups
  Details will be sent out soon

## Slide 25: Other policies
Details on the course webpage
Don’t cheat
https://www.erg.cuhk.edu.hk/erg/AcademicHonesty
Consult this booklet from our faculty
  https://www.erg.cuhk.edu.hk/erg/sites/default/files/Disciplinary_Booklet_2024-25%20(final).pdf

## Slide 26: Let’s Talk Internet

## Slide 27: The Internet consists of many end-systems
end-system
Windows PC
Linux server
MAC laptop
car navigator
sensor
smartphone
tablet

## Slide 28: Connected by switches
switch
end-system

## Slide 29: And links
phone lines
link
fibers
cable TV lines
wireless links
switch
end-system

## Slide 30: Managed by many parties
Internet Service Provider
phone company
cable company
university net
link
switch
end-system

## Slide 31: Transfers data
switch
data
path
Internet Service Provider
link
end-system

## Slide 32: A federated system
The Internet ties together different networks by the IP protocol
  A common interface binds them all together
HKBN
China Mobile
PCCW

## Slide 33: Connecting everyone
Any two end-hosts (anywhere!) can talk to each other via the Internet
Q: how to connect millions of millions of nets?
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 34: Connecting everyone
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
connecting each network to each other directly doesn’t scale: O(N2) connections.

## Slide 35: Solution: Switched networks
End-systems and networks connected by switches instead of directly connecting them
  Why?
Allows us to scale!
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…

## Slide 36: When do we need to share the network?
Switch and link resources

## Slide 37: Shared among many services
Zoom client
Zoom client
Xiaohongshu server
Firefox accessing instagram
Netflix client
Netflix server

## Slide 38: Two ways to share
Circuit switching
  Resource reserved per connection
Packet switching via statistical multiplexing
  Packets treated independently, on-demand

## Slide 39: Circuit switching
src sends reservation request to dst
Switches create circuit after admission control
src sends data
src sends teardown request
More details in backup
dst
src
10 Mbps?
10 Mbps?
✔️
✔️

## Slide 40: Circuit switching
Reservation establishes a “circuit” within a switch
switch
src
dst

## Slide 41: Circuit switching
Pros
  Predictable performance
  Simple/fast switching (once circuit established)
Cons
  Complexity of circuit setup/teardown
  Circuit setup adds delay
  Switch fails  its circuit(s) fails
  Extremely inefficient when traffic is bursty!
    Think: Are you always clicking?

## Slide 42: Packet switching
Each packet contains destination (dst)
Each packet treated independently
switch
dst

## Slide 43: Packet switching
Each packet contains destination (dst)
Each packet treated independently
With buffers to absolve transient overloads
switch
dst

## Slide 44: Packet switching
Pros
  Efficient use of network resources
  Simpler to implement
  Robust: can “route around trouble”
Cons
  Unpredictable performance
  Requires buffer management and congestion control

## Slide 45: Statistical multiplexing
Allowing more demands than the network can handle
  Hoping that not all demands are required at the same time
  Results in unpredictability
  Works well except for the extreme cases

## Slide 46: MASSIVE Scale
4.6 Billion users
>1.8 Billion websites
>200 Billion emails sent per day
>2.5 Billion smartphones
>2.7 Billion Facebook users
>1 Billion hours of YouTube watched per day
Routers that switch 10 Terabits/second
Links that carry 400 Gigabits/second
Notes: https://www.internetlivestats.com

## Slide 47: Google’s TPU cluster (pod)

## Slide 48: Have we found the right solution?
We don’t really know…
What we do know
  The early Internet pioneers came up with a solution that was successful beyond all imagining
  Several enduring architectural principles and practices emerged from their work
Still, it is just one design with many questions

## Slide 49: The Internet is a lesson
In how to reason through the design of a very complex system
  What are our goals and constraints?
  What’s the right prioritization of goals?
  How do we decompose a problem?
  Who does what? How?
  What are the interfaces between components?
  What are the tradeoffs between design options?

## Slide 50: How do we evaluate a network?

## Slide 51: Performance metrics
Delay
Loss
Throughput

## Slide 52: Delay
How long does it take to send a packet from its source to destination?

## Slide 53: Delay
Consists of four components
  Transmission delay
  Propagation delay
  Queuing delay
  Processing delay
due to link properties
due to traffic mix and
switch internals

## Slide 54: A network link
Link bandwidth
  Number of bits sent/received per unit time (bits/sec or bps)
Propagation delay
  Time for one bit to move through the link (seconds)
BDP, bandwidth-delay product
bandwidth
Propagation delay
delay x bandwidth

## Slide 55: 1. Transmission delay
How long does it take to push all the bits of a packet into a link?
Packet size / Transmission rate of the link
  E.g., 1000 bits / 100 Mbits per sec = 10-5 sec

## Slide 56: 2. Propagation delay
How long does it take to move one bit from one end of a link to the other?
Link length / Propagation speed of link
  E.g., 30 kilometers / 3*108 meters per sec = 10-4 sec

## Slide 57: Packet delay Sending a 100-byte packet
time=0
A
B
100Byte packet
Time
1Mbps, 1ms
Time to transmit one bit = 1/106s
Time to transmit 800 bits=800x1/106s
Time when that bit reaches B = 1/106+1/103s
The last bit reaches B at
(800x1/106)+1/103s
= 1.8ms

## Slide 58: Packet delay Sending a 100-byte packet
time=0
A
B
100Byte packet
Time
1Gbps, 1ms
Time to transmit one bit = 1/109s
Time to transmit 800 bits=800x1/109s
Time when that bit reaches B = 1/109+1/103s
The last bit reaches B at
(800x1/109)+1/103s
= 1.0008ms

## Slide 59: Sending a large file using 100-byte packets
100Byte packet
100Byte packet
A
B
100Byte packet
1Gbps, 1ms

## Slide 60: Pipe view of a link
Transmission delay decreases as bandwidth increases
time
bandwidth
transmission delay

## Slide 61: 3. Queuing delay
How long does a packet have to sit in a buffer before it is processed?

## Slide 62: Queuing delay: “pipe” view

## Slide 63: Queueing delay: “pipe” view
No overload!

## Slide 64: Queueing delay: “pipe” view
Transient Overload
Not a rare event!
Queue

## Slide 65: Queueing delay: “pipe” view
Queue
Transient Overload

## Slide 66: Queueing delay: “pipe” view
Queue
Transient Overload

## Slide 67: Queueing delay: “pipe” view
Queue
Transient Overload

## Slide 68: Queueing delay: “pipe” view
Queue
Transient Overload

## Slide 69: Persistent overload leads to packet drop/loss
Queue

## Slide 70: Queueing delay
How long does a packet have to sit in a buffer before it is processed?
Depends on traffic pattern
  Arrival rate at the queue
  Nature of arriving traffic (bursty or not?)
  Transmission rate of outgoing link

## Slide 71: Queueing delay
How long does a packet have to sit in a buffer before it is processed?
Characterized with statistical measures
  Average queuing delay
  Variance of queuing delay
  Probability delay exceeds a threshold value

## Slide 72: Basic queueing theory terminology
Arrival process: how packets arrive
  Average rate A
W: average time packets wait in the queue
  W for “waiting time”
L: average number of packets waiting in the queue
  L for “length of queue”

## Slide 73: Little’s Law (1961)
L = A x W
Compute L: count packets in queue every second
Why do you care?
  Easy to compute L, harder to compute W
Notes: Row vs column

## Slide 74: 4. Processing Delay
How long does the switch take to process a packet?
  Negligible

## Slide 75: End-to-end delay
transmission
propagation
queueing
processing
transmission
propagation
queueing
processing
transmission
propagation

## Slide 76: Round Trip Time (RTT)
Time for a packet to go from a source to a destination and to come back
Why do we care?
  Measuring delay is hard from one end
RTT/2 equals average end-to-end delay
  Why not exact?

## Slide 77: Loss
What fraction of the packets sent to a destination are dropped?

## Slide 78: Throughput
At what rate is the destination receiving data from the source

## Slide 79: Throughput
F/R + propagation delay
Transmission rate R bits/sec
Average throughput =
Transfer time (T) =
File of size F bits
F/T ≈ R
Packets of size L bits

## Slide 80: End-to-end throughput
Transmission rate R
File of size F bits
Packets of size L bits
Transmission rate R’ > R
Average throughput =
min{R, R’} = R
bottleneck link

## Slide 81: Summary
How is the network shared?
  On-demand or via reservation
How do we evaluate a network?
  Bandwidth, delay, loss, …
BDP
  See backup slides

## Slide 83: A network link: BDP
Link bandwidth
  Number of bits sent/received per unit time (bits/sec or bps)
Propagation delay
  Time for one bit to move through the link (seconds)
Bandwidth-Delay Product (BDP)
  Number of bits “in flight” at any time
BDP = bandwidth × propagation delay
bandwidth
Propagation delay
delay x bandwidth

## Slide 84: BDP Examples
Same city over a slow link:
  Bandwidth: ~100Mbps
  Propagation delay: ~0.1msec
  BDP: 10,000bits (1.25KBytes)
Cross-country over fast link:
  Bandwidth: ~10Gbps
  Propagation delay: ~10msec
  BDP: 108bits (12.5MBytes)